## Slide 1: Compressed Air
The Heart or the Cancer?
Compressed air systems and accessories
for removing debris and moisture before entry into pneumatic pumps

## Slide 2
  Typical System Issue – Water!
  Compressed Air Systems
  Air/Water filtration
  Water/Moisture removal
Discussion – Topics to address
Notes: Review the course contents.

## Slide 3
A 200 HP compressor operating in a climate of 60°F with 40 percent relative humidity will generate approximately 50 gallons of condensate a day. However, that same compressor operating in a climate of 90°F with 70 percent relative humidity will generate approximately 260 gallons of condensate a day
Compressed Air & Moisture – The Enemy
Notes: Have one of the participants read the slide. Discuss the importance of compressor maintenance and filter (water traps - minimum defense).

## Slide 4
Outcome & Solution – How bad can it get?

## Slide 5
  Debris and Moisture generated in an air system can cause premature pump failure, air tool failure, and compressor failure.
  Air filtration and moisture separation is the key to long term equipment reliability & compressor performance.
  Most shops require a large volume of air. Failure of the compressor, pumps, pneumatic equipment stops business in its tracks!
  Air compressor and equipment break downs cause serious shop disruptions that cost $$$ in repairs and down-time.
The Air System – Importance
Notes: All air operated pumps are assembled using grease as a lubricant. Water introduced from the air system can prematurely wash the grease from the air motor causing premature pump failure.
Correctly sizing the compressor to the application is the 1st step to minimizing water in the system.
Correctly sizing the filter to the application is the 2nd step to minimizing water in the system.
Proper daily and weekly maintenance which includes draining the compressor tank and drop legs is the 3rd step in minimizing water in the system.
The #1 cause for a pump failure is water in the air motor……and it is not covered under warranty!

## Slide 6
Size your system properly
  An electric compressor will generate 5 CFM/HP generally
  Install the correct pipe system
    Proper pipe or tubing sized to volume required
    Drip leg to catch water – to be drained daily (Minimum)
    Drops to pneumatic equipment and tools face upward
    Air Main slants back towards the compressor with manual tank drain (Minimum)
  Install air filter and MOISTURE separator to protect your investment
    Air filter removes dust, dirt, rust and other particles; poor at removing moisture!
    Water Filtration BEST method to remove moisture molecules
      Manual tank drains – most affordable; Auto-drain is preferred method
      Manual water traps/drop leg – most affordable method, BUT …
      Best solution to protecting the pneumatic pumps is a Liquid Separator
      Other more expensive solutions – Aftercooler/separator remove about 70% moisture and for even dryer air the addition of a desiccant dryer may be needed but both options work well but at a cost. DO you need this?
The Air System – Minimizing Debris & Moisture
Notes: -Reiterate the comments from the previous slide.
It is important to note that an in-line-filter is not the same as a moisture separate. The filter will catch water in its liquid state, but water molecules in their vapor state are small enough to flow through most air filters.

## Slide 7
Looped Air System – With Drop Legs
Liquid
Separator
Notes: Note the slope of the main air line to allow moisture to drain from the system.
Note the design of the air drops to not allow moisture to drain back to pumps or air tools.
- Automotive air systems typically do not include dessicate or refrigerated air dryers.

## Slide 8
Compressed Air Supply – Pump Layout
Bleed-type master air valves relieve air trapped between the valve and downstream components. Prevents pump from unexpected cycling.
Ball valve for releasing collected moisture in header
Pump overrun valve stops pump when tank empty or downstream hose leak. Not required if low-level cut-off is used.
Size pump air supply hose to at least equal to the pump air inlet fitting size. Quick Disconnects can restrict air flow impacting pump performance.
Filter, Regulator and Lubricator. Filter and regulator recommended. Lubricator recommended only if properly maintained or specified.
Use air hose between header and pump to prevent air leakage at fittings due to pump vibration. Do not hard plumb the air line to the motor. On new systems distributor to obtain system air pressure and volume available.

## Slide 9
Comparison – Why a Liquid Separator over an Air Filter?
Operation
  Air enters the Liquid Separator inlet and turns into the Separator module. The inlet of the separator module contains a set of fixed vanes which the air pass through
  The vanes force the air to spin inside the vessel, the spinning air is then forced to change direction as it passes the impinger
  A vortex is created; which narrows and intensifies as it reaches the lower part of the separator module
  Bulk liquid is removed from the airstream due to:
    Directional changes of airstream
    Velocity changes
    Centrifugal action of the vortex
  As the vortex reaches the bottom of the module, air is forced through the center of the vortex
  Aerospace turning vanes, located in the outlet, turn the inefficient corner into beneficial motion. The turning vanes reduce turbulence, minimizing pressure loss and increase air output efficiency

## Slide 10
  Ball valve - Pressure relieving - isolates pneumatic pump for after hours safety and ease of repair
  Valve - Over-run control - Control SCFM flow to Grease pumps. Senses dramatic increase in air flow and shut off air supply to pump
  Filter - reduces solid contaminants - such as dust, dirt, rust scale etc. from entering the pump
  Separator Liquid - removes moisture - before entering into pneumatic pump
  Regulator - regulates air pressure - to pneumatic pump based on viscosity of fluid and flow needed and should be set between 40-80 psi
  Lubricator - injects lubricant - into air stream and should only be used where maintenance prevention is established and maintained
Components – Beneficial Air System Components
Notes: Describe the critical components and their function.
Balcrank recommends including a check valve be placed on the bottom of the down tube for applications greater than 42” vertical lift.
The air supply components (air hose and FLR) should match the air requirements of the pump.
Filter/Regulators are required for warranty.
Lubricators are only recommended when specified or under extreme conditions. If used, the lubricator must be maintained and adjusted properly using 10W non-detergent only.
Pressure relief must be installed in hard piped systems. Lack of pressure relief valves can cause tips, hose reel swivels, and the hose to burst in extreme conditions.
Ball valve locations should include air supply to the pump, out-bound fluid supply to piping, and all hose reels.
The inclusion of the suggested air and fluid components can add significantly to your sales and commissions!

## Slide 11: Components – Typical Oil System Components
When assembling a system BOM, follow the trail of the oil from pump intake to dispense point
C – Liquid Separator
3260-067 ½” NPT(F)
3260-068 ¾” NPT(F)
3260-069 1” NPT(F)